## Slide 1: Vehicle-to-Vehicle Communication using Visible Light
- Preethika M

## Slide 2: Abstract
Demonstrates Vehicle-to-Vehicle (V2V) communication using Visible Light Communication (VLC).
LED used as transmitter and Photodiode as receiver.
Arduino microcontroller processes sensor data and transmits via optical signals.
Provides secure, interference-free, and low-cost alternative to RF-based systems.

## Slide 3: Problem Statement & Need
Current V2V systems rely on RF (Wi-Fi, DSRC) → prone to congestion,
interference, hacking.
Growing traffic → need for reliable, fast, and safe data sharing between
vehicles.
VLC offers high bandwidth, security, and no RF interference.

## Slide 4: Objectives
Implement data transmission between two vehicles using visible light.
Encode vehicle motion (velocity/acceleration) into LED pulses.
Decode at receiver side using photodiode + Arduino.
Demonstrate feasibility of VLC in transportation safety.

## Slide 5: Literature Survey
Existing V2V (RF-based):
  DSRC, Wi-Fi, Bluetooth, 5G → provide wireless links.
Disadvantages:
  Congestion in crowded areas.
  Security risks (hacking/jamming).
  Limited bandwidth in RF spectrum.

## Slide 6: Proposed System
Use Visible Light as medium.
Arduino + Accelerometer to sense vehicle motion.
LED (Tx) transmits encoded pulses.
Photodiode (Rx) detects and decodes pulses.
More secure (line-of-sight), higher bandwidth, no EM interference.

## Slide 7: System Overview
Input: Vehicle acceleration (MPU6050).
Processing: Arduino calculates velocity.
Transmission: LED encodes velocity → light pulses.
Reception: Photodiode receives pulses → Arduino decodes.
Output: Vehicle 2 displays velocity info → collision avoidance.

## Slide 8: Key Components Integrated
Arduino Uno
MPU6050 Accelerometer
LED (Transmitter)
Photodiode BPW34 (Receiver)
Resistors, breadboard, jumper wires

## Slide 9: Block Diagram

## Slide 10: Hardware & Software
  Hardware:
  Arduino UNO
  MPU6050
  LED
  Photodiode
  Resistors
  Wires
  Software:
  Arduino IDE

## Slide 11: Hardware Setup
Vehicle 1: Arduino + MPU6050 + LED (Tx)
Vehicle 2: Arduino + Photodiode (Rx)
LED → Photodiode line-of-sight
Serial Monitor for velocity output

## Slide 12: Working Principle
Acceleration measured by MPU6050 → Arduino calculates velocity.
Velocity encoded into LED blinks (PWM).
Photodiode detects pulses → converts to electrical signals.
Receiver Arduino decodes → displays velocity data.

## Slide 13: Code Snippet
Transmitter (Arduino):
  int ledPin = 9;
  void loop() {
  int velocity = 60; // Example
  int freq = map(velocity, 0, 200, 1000, 100);
  digitalWrite(ledPin, HIGH);
  delayMicroseconds(freq);
  digitalWrite(ledPin, LOW);
  delayMicroseconds(freq);
  }
Receiver (Arduino):
  int sensorValue = analogRead(A0);
  if(sensorValue > 100)
  Serial.println("Light pulse detected → Vehicle moving");
  else
  Serial.println("No pulse → Vehicle stopped");

## Slide 14: Outputs
Transmitter:
  LED blinking with velocity info.
Receiver:
  Serial monitor shows →
    "Vehicle moving" when pulses detected.
    "Vehicle stopped" when no pulses.

## Slide 15: Applications
Vehicle collision avoidance.
Intelligent traffic management.
Platooning (convoy of vehicles).
Secure vehicle data exchange (speed, braking info).

## Slide 16: Future Enhancements
Use high-power LEDs for longer range.
Advanced modulation schemes (OOK, PWM, OFDM).
Integration with real cars.
Combine VLC with 5G for hybrid V2V systems.

## Slide 17: Conclusion
VLC provides secure, interference-free, and high-speed communication.
Demonstrated working V2V prototype using Arduino, LED, and
photodiode.
Strong potential for future intelligent transportation systems.